## Slide 1: MICROWAVE RADIOMETER (MWR) EVALUATION OF MULTI-BEAM SATELLITE ANTENNA BORESIGHT POINTING USING LAND-WATER CROSSINGS, FOR THE AQUARIUS/SAC-D MISSION
by Bradley Clymer
March 25, 2015
UCF CFRSL

## Slide 2: Thesis Objective
Develop an algorithm to perform a quantitative evaluation of the geolocation accuracy of Microwave Radiometer (MWR) multi-beam footprints on the earth’s surface
Deliver statistical data to the CONAE for corrective action in future data processing
  Process at least one year of MWR data and perform a statistical assessment of all individual beam footprints geolocation errors for (8 beams 3 frequency/polarization combinations)

## Slide 3: Aquarius/SAC-D Overview
NASA Aquarius instrument
  Microwave radiometer/scatterometer
  Operates at L-band (1.4 GHz)
  3 beam IFOV’s (~ 150 km diameter) perpendicular to line of flight
  380 km swath width
CONAE MWR Instrument
  Provides geophysical retrievals that are collocated with AQ 3-beam footprints
  K- (H-pol) and Ka-band (V&H-pol)
  8 beams forward (Ka-band), 8 beams aft (K-band)

## Slide 4: Instrument Geometry - Aquarius
AQ beam geometry
3 Beams cross-track (azimuth 90o)
IFOV size:
  79x94 km – 96x156 km
380 km swath
AQ/SAC-D
Sun-synchronous polar orbiting satellite
AQ radiometer/scatterometer utilizes an offset parabolic reflector antenna in a pushbroom configuration

## Slide 5: Instrument Geometry - MWR
MWR forward-looking beams
8 beams (Ka-band, V- & H-pol)
Fixed beams on conical arcs
  Earth Incidence: 52o and 58o
IFOV size range: 25 x 50 – 30 x 60 km
MWR aft-looking beams
8 beams (K-band, H-pol)
Earth Incidence: 52o and 58o conical arcs
IFOV identical to forward beams

## Slide 6: MWR Measurements – One Day
High contrast brightness temperature from ocean to land: maximum slope occurs at coastline and indicates ‘sensor observed’ boundary
Oribital cycle: 7 days – exact repeat
Width shown represents swath of all eight beams

## Slide 7: Past Work – 2004 SSM/I Radiometer Imager
High resolution Tb images compared to coastal maps to determine mispointing
Adjustment of satellite attitude: roll, pitch & yaw to determine “best pointing”
Before
Correction
After
Correction

## Slide 8: Past Work – 2006 WindSat Imaging Radiometer
Used Tb gradients to estimate land/water boundaries
Adjusted satellite roll and pitch to register image with coastline maps
Before
Correction
After
Correction

## Slide 9: Past Work: Catherine May EE MS Thesis 2012, Engineering Evaluation Of Multi-beam Satellite Antenna Boresight Pointing Using Land/Water Crossings
Developed algorithm to determine MWR radiometer footprint geolocation at land/water boundaries relative to high resolution coastline maps
Used individual beam crossings with CONAE calculated IFOV centers
Processed ~ 3 months of MWR data
  Manually picked supersites to show efficacy of slope technique
  Produced sample datasets to calculate statistical geolocation errors for various antenna beams
Notes: Assumption was 50% beam fill was max slope, mostly done by hand, did just enough to show proof-of-concept

## Slide 10: Past Work: Catherine May EE MS Thesis 2012,
Developed theoretical radiometer model
An Ideal radiomentric land/water boundary,
When colvolved with an ideal 1D Gaussian beam pattern,
Produces a Sigmoid curve of apparent brightness temperatures,
The derivative of which is a Gaussian curve
[km]
ocean
Land
Notes: Assumption was 50% beam fill was max slope, mostly done by hand, did just enough to show proof-of-concept

## Slide 11: Current Work
Implemented 2D MWR antenna pattern convolution of actual Tb coastline images to validate the 1D assumptions of 50% beam-fill = max Tb slope (C. May Thesis 2012)
  Showed that 50% beam-fill was insensitive to orientation of elliptical IFOV axes relative to coastline crossing
  Implemented improved geolocation error calculation (closest point to coastline)
Automated “SuperSite selection” to allow for large datasets to be generated (MatLab/Google Earth Link)
Performed one-year data processing (full seasonal cycle) and collected statistics of collocation error (km) for all 24 beams for asc and desc orbit passes

## Slide 12: 2D Theoretical MWR convolution vs. Measured Tb series
Theory
MWR measured

## Slide 13: Brightness Temperatures Over a Coast
Water on left, land on right
Beam efficiency picks up incremental increase in radiated power
Gaussian ellipse approximation to more complex beam pattern
Steepest slope occurs at 50% beam-fill
50% fill point

## Slide 14: What is a supersite?
Real-world land/water coastlines that have good characteristics
  Long straight coastlines > IFOV dimensions
  locus of IFOV center locations with ±45°crossing angles of coast
  Dry land without major inland water
  No significant man-made objects (roads, buildings, etc.)
  Madagascar Coast example

## Slide 15: Super Site Locations for Geolocation Analysis
Below are examples of SuperSites selected for a single beam and polarization – 37V – ascending
On average, 7-20 sites for each of 8 beams
Notes: Will be discussing where satellite crossings go over

## Slide 16: Algorithm for Calculating Instrument-Observed Coast
Interpolate Lat/Long of Vertex
Calculate Distance to Nearest Coastal Point
Aggregate Results by Site, Beam, and Polarization
Check Data Lat/Long for SuperSite Proximity
Difference Sequential
Fit Parabola to Neighborhood of Maximum Difference
Calculate Parabola Vertex

## Slide 17: Select data from SuperSite region
Pre-select bounding box region
Typically ten to twelve geolocated

## Slide 18: Fit least-squares parabola to neighborhood of maximum
Differences of successive points define slopes (yellow and green)
Parabola Maximum fits slopes
Vertex of Parabola defines crossing point
Note that nearly ideal case shows vertex closely aligned to an IFOV center
Fit Parabola
Derivatives

## Slide 19: Difference assign slope location between points
Note that differences lie between
Typically 4-6 samples used for fitting

## Slide 20
Interpolate vertex to a lat/long between data, find nearest coast
Geolocation
error
Notes: This slide has about a million parts, DANGEROUS TO MOVE ANYTHING

## Slide 21: Supersite Selection Algorithm
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node

## Slide 22: SuperSite Finding Algorithm: Step 5
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node
Threshold
Samples

## Slide 23: Supersite Selection Advances
Bulk Processing with minimal oversight
Evaluate visual fitness in Google Earth
Automated kml interface allows rapid selection and simple (yes/[]) input
Average of 16 supersites per beam and polarization

## Slide 24: MWR Geolocation Results

## Slide 25: B1 Ascending Supersite No. 1, 14 AQ cycles
IFOV
trajectory
V- & H-pol
Google Earth View
CONAE V- & H-
Boresight pointing
Typical
MWR
IFOV
Tb slopes vs. distance
V-pol & H-pol

## Slide 26: Error Analysis Results by Beam, 1-8
23H
37H
37V
Notes: Chart of mean and STD vs. beam #, with error bars
Average location error Show plots of consistency between V & H, spatial collocation plot, consistent difference, V&H Disparity Table with 24 beams, mean error, columns are beam, rows are pols, mean error/std, one decimal place Histogram for consistency

## Slide 27: 37V & H Comparison by Beam, 1-8
Difference: 37H – 37V
37V
37H

## Slide 28: Geolocation Histograms for 8 beams 37V

## Slide 29: Results Table
 | Beam 5 |  |  |  | Beam 6 |  |  |  | Beam 7 |  |  |  | Beam 8 |  | 
 | Median Error | Error Std. Dev | N |  | Median Error | Error Std. Dev | N |  | Median Error | Error Std. Dev | N |  | Median Error | Error Std. Dev | N
36.5V | M=1.2 | σ=2.4 | n=790 |  | M=2.7 | σ=2.0 | n=745 |  | M=5.2 | σ=3.9 | n=920 |  | M=3.8 | σ=4.1 | n=486
36.5H | M=2.7 | σ=3.2 | n=1076 |  | M=1.9 | σ=4.2 | n=1196 |  | M=4.6 | σ=4.6 | n=1032 |  | M=4.8 | σ=2.4 | n=763
23.8H | M=1.6 | σ=5.6 | n=712 |  | M=-.3 | σ=6.3 | n=561 |  | M=1.0 | σ=1.9 | n=316 |  | M=.8 | σ=3.9 | n=522
 | Beam 1 |  |  |  | Beam 2 |  |  |  | Beam 3 |  |  |  | Beam 4 |  | 
 | Median Error | Error Std. Dev | N |  | Median Error | Error Std. Dev | N |  | Median Error | Error Std. Dev | N |  | Median Error | Error Std. Dev | N
36.5V | M=1.9 | σ=4.3 | n=699 |  | M=6.8 | σ=2.0 | n=483 |  | M=4.2 | σ=3.7 | n=1100 |  | M=2.4 | σ=1.9 | n=722
36.5H | M=4.7 | σ=4.5 | n=1193 |  | M=5.3 | σ=5.4 | n=802 |  | M=3.0 | σ=2.4 | n=1020 |  | M=3.2 | σ=4.1 | n=989
23.8H | M=1.6 | σ=3.7 | n=511 |  | M=-0.2 | σ=5.5 | n=441 |  | M=-1.1 | σ=3.5 | n=700 |  | M=-0.9 | σ=2.2 | n=536
*All errors in units of kilometers

## Slide 30: Conclusions: All thesis objectives met!
Objective: Create algorithm to calculate MWR geolocation error
  Implemented max-slope algorithm and verified 50% beam-fill using 2D MWR antenna pattern convolutions against real Tb images of land/water coast
Objective: Develop software package to analyze MWR orbit data
  22,000 lines of code
  Refined processing time from four days to three hours to process one-year data
Objective: Process at least one-year of data (full seasonal cycle) to generate statistics
  3-year data record will be processed by thesis completion
Objective: Generate statistical database of mispointing errors for CONAE use
  Preliminary processing complete for one-year, additional analysis to be completed by thesis completion

## Slide 31: Future Work
Analysis of collocation histograms to determine systematic effects
  Ascending & descending orbital passes
  Orientation of IFOV elliptical axis relative to coastline
  Apparent pointing error for 37H & 37V beams
Conversion of geolocation error (km) to antenna pointing angles: azimuth and elevation
Validation of beam pointing results using Deep space calibration (transitions between earth limb & space)
Notes: Error analysis of uncertainty, **add to paper**, one example from each set of beams

## Slide 32: Publications
Conference
[1] B. Clymer, C. May, L. Schneider, F. Madero, M. LaBanda, M. Jacob and W. Jones, 'Microwave Radiometer (MWR) Beam-Pointing Validation for the Aquarius/SAC-D Mission', in MicroRad, United States, 2014.
[2] B. Clymer, 'MicroWave Radiometer Beam-Pointing Validation for the Aquarius/SAC-D Mission', in Aquarius Science Team Meeting, Seattle, WA, 2015.
Journal
B. Clymer, F. Madero, M. Jacob, W. Jones and C. May, 'Microwave Radiometer (MWR) Evaluation Of Multi-beam Satellite Antenna Boresight Pointing Using Land/Water Crossings For The Aquarius/SAC-D Mission', JSTARS - Journal of Selected Topics in Applied Earth Observations and Remote Sensing, vol. 8. Under Review
Notes: Shoot for 30

## Slide 33
END

## Slide 34: Back-Up Slides
Backup
Notes: Some of Nick’s charts

## Slide 35: References
[1]B. Tieu and M. Suarez, "Mission Plan, Tech. Report AS-213-0097, 2009," Buenos Aires, Argentina, 2009.
[2]Gallery. (n.d.). Retrieved March 17, 2015, from http://aquarius.umaine.edu/cgi/gallery.htm
[3]Aquarius/SAC-D Project Overview. (2011, June 1). Retrieved March 12, 2015, from http://aquarius.nasa.gov/pdfs/mission_summary.pdf
[4]Heliosynchronous Orbit Graphic - "Heliosynchronous orbit" by Heliosynchronous_Orbit.png: BrandirXZise - This file was derived from: Heliosynchronous Orbit.png:. Licensed under CC BY-SA 3.0 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Heliosynchronous_orbit.svg#/media/File:Heliosynchronous_orbit.svg
[5] May, C. (2012). Engineering evaluation of multi-beam satellite antenna boresight pointing using land/water crossings. Orlando, Fla.: University of Central Florida.
Omit or put into back-up

## Slide 44: Brightness Temperatures Over a Coast
Water on left, land on right
Beam efficiency picks up incremental increase in radiated power
Gaussian ellipse approximation to more complex beam pattern
Notes: Animation of Ellipses

## Slide 45: SuperSite Finding Algorithm: Step 1
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node
I guess that you want to show how you automated the process. OK, this is good, but it’s not the most important thing that you did! Devoting more than 1 or 2 slides is too many.
Notes: Backup charts, down to one or two

## Slide 46: SuperSite Finding Algorithm: Step 2
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node

## Slide 47: SuperSite Finding Algorithm: Step 3
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node

## Slide 48: SuperSite Finding Algorithm: Step 4
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node

## Slide 49: SuperSite Finding Algorithm: Step 5
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node

## Slide 50: SuperSite Finding Algorithm: Step 5
Classify each orbit by ascending node
Aggregate orbits into matrices
Take column-wise mean of each matrix
Difference each of 103 time series to find slope
Evaluate sites above desired threshold heuristically
Align matrices by ascending node
Threshold

## Slide 51: Lines of Code

## Slide 52: 37V Antenna Pattern

## Slide 53
Thesis Organization
  Research Obj – OK as revised - Done
  Intro – combine 5 & 6 into one slide – the science in NOT important - Done
  AQ/MWR geometry – slides 7, 8, 9 are OK as revised
  Related Past work –
    not good! Make a slide/past work and give detail of how they did it (NOT #”s results). If possible make one slide and not two.
    Present Cathy’s thesis summary of what she did. Her work was more of a “proof of concept” for MWR and preliminary #’s for geoloc errors
  What you did! - Present a bullet slide of what you did to extend this research beyond Cathy May
  Technique description
    slide -12 is Cathy’s hypothesis based ion 1D convolution of a Gaussian ant beam with a step function land/water boundary
    Insert a slide on the 2D ant pattern convolution that you performed to demonstrate the the max slope point is the 50% land/50% water for the IFOV (insensitive the the alignment of the ellipse relative to the coast line.
    Slide-13 is OK but there are some issues listed on the slide (make this the lowest priority to fix).
  Algorithm description
    Slides 14 – 18 are OK with comments considered, but slide – 19 misses the mark (see comments)
    Slides 20 – 29 are not good and put too much emphasis on a minor point – see my comments to reduce to 2-3 slides.
  Results
    Slides 30 – 32 are OK but you need to add more results – see my notes on 32. This should be 5 – 8 slides
  Conclusions – will come after reviewing your presentation – Monday afternoon or early evening.